### Form 4: Regulations on the Booth Construction of Large Exhibition

In view of the fact that in the present exhibition sector there are wide differences in strength and qualification among companies providing services for construction of exhibition stands, and in order to ensure the standardized construction of exhibition stands for various conventions and exhibitions of Shanghai New International Expo Center (SNIEC), as well as the personal safety and property security of both exhibitors and visitors, after consultation with HAH Consulting & Exhibition Co., Ltd. Shanghai (HAH), we have jointly formulated the following detailed management rules, so as to implement uniform review and supervision over the design, structure, construction and disassembly of participating exhibition stands.

Formality for construction of indoor specially structured exhibition stands:

1．For all specially structured exhibition stands, the design drawings of its stand construction must be submitted to SINEC & HAH for review. The drawings subject to review include:

a. 	Booth perspective drawing (1 front-side and 2 sides)

b. 	Ground floor plan

c. 	Structural diagram

d.  Structural calculation sheet and load calculation picture

e. 	Circuit diagram

f. 	Detailed structural diagram

g. 	Section and four sides pictures

h. 	Detailed booth material checklist

All drawings must be marked with the axis size of beams and posts, as well as specifications and sizes of all structural materials.

2. All construction institutions entering the exhibition hall to start stand construction must provide SINEC & HAH with copies of their business license certificate along with license certificate for special job types imprinted with company seal, which will be used for filing purpose.

3. All construction employees entering the exhibition hall to start stand construction must pay a risk deposit for exhibition stand (this deposit shall be paid in cash or check); if no safety accident occurs to the exhibition stand during the exhibition period, the deposit will be returned in view of the clearing and transport conditions of the exhibition stand at the site after the exhibition is over.

Management regulations for construction of indoor specially structured exhibition stands:

- The structure of all specially structured exhibition stands must be reasonably designed, so as to ensure security and safety of the constructed structure. The construction materials shall use non-inflammable or fire retardant materials.

- The designed structural strengths of all exhibition stands shall meet the strength required by the load, during the construction period efforts shall be made to ensure the overall strength, stiffness, stability and local stability of the exhibition stand structure.

- The area of exhibition stand constructed by each construction institution must comply with the area specified in the submitted application. The area of an exhibition stand constructed by construction institutions shall not exceed the leased area, and its projected side line must not extend beyond the leasing border line.

- For exhibition stand structures decorated with glass ornaments, the glass must use safety glass, so as to ensure security in construction and installation, and marked with conspicuous signs in order to prevent glass breaking to cause personal injury or death.

- For exhibition stand using steel structure standing post, the standing post shall use welding-free material with a diameter of over 100mm, its bottom shall be welded with a secure base, with a flange welded onto its upper structure to increase its load bearing area of the standing post, so as to ensure the soundness of exhibition stand structure.

- The ground contact width of the main load-bearing wall in all exhibition stand structures shall not be less than 120mm, so as to ensure the contact area between wall body and the ground.  For walls with a large span of over 6m and steel column framework structures, connecting beams shall be added on the top, with supports fitted in between the columns at the bottom of columns, so as to ensure the overall stiffness and stability of the exhibition stand.

- For construction of all exhibition stands in which the structural designs involve stage or platform structure with a height of over 1.2 m, as well as all indoor two-deck, multiple-deck or complicatedly structured exhibition stands, their exhibition stand structural drawings must be provided, which shall be imprinted with seals of National Grade A Registered Structural Engineer for confirmation, accompanied by structural calculation sheet. All exhibitors and construction institutions shall give full consideration to the safety of exhibition stand from design to construction, so as to ensure the soundness of each connecting joints of the exhibition stand and the overall structure of the exhibition stand.

- Construction of double-deck or multiple-deck exhibition stand must be equipped with fire extinguishers that have passed annual inspection.

- All structural back walls of neighboring exhibition stands must be properly decorated.

It is strictly prohibited for indoor exhibition stands to adopt totally enclosed type ceilings. Exhibition stand ceilings must not obstruct the fire-fighting facilities on the top of the exhibition hall. It must also be ensured that the ceiling shall have an raw space of over 50% of its total area, so as to ensure the fire prevention safety of the exhibition stand.

# Text boxes

Form 4